## Slide 1: Unit 9. Introduction to MIMO
EL-GY 6023. Wireless Communications
Prof. Sundeep rangan

## Slide 2: Learning Objectives
Assuming CSI-R and CSI-T, describe the diagonalization of a MIMO channel
  Compute the virtual directions and their SNRs
Compute the capacity for a MIMO channel using diagonalization
  Narrowband and wideband
Mathematically formulate the power allocation problem and find optimal power allocations
Describe linear receivers, identify the main blocks and compute their capacity
  Zero forcing and LMMSE
Describe reference signals for MIMO channel estimation in 4G and 5G systems
Compute optimal statistical pre-coders and compute the capacity

## Slide 3: Excellent Text for This Section
Some material in this section is from this recent text
Provides excellent:
  Information theoretic background
  Practical guidelines for implementation
  Up-to-date examples with issues for mmWave
We only cover a small section
  Single user MIMO
  Many derivations are left for the text

## Slide 4: Outline
Spatial Multiplexing with CSI-T and CSI-R
Power Allocation and Rank Selection
Spatial Multiplexing with CSI-R Only
Channel Estimation and CSI-R
CSI-T Feedback and Statistical Pre-Coding

## Slide 5: Spatial Multiplexing
Many environments have multiple spatial paths
  LOS, reflections, diffraction, …
Spatial multiplexing concept
  Transmit separate information streams on different paths
Increases degrees of freedom
Requires:
  Channel rank where is the number of streams
  In particular,
  Also need sufficient power for the streams
TX array
RX array

## Slide 6: MIMO History
Early research:
  ArrayComm 1991
  Paulraj and Kailath, initial patent on SDMA
  Foschini and others, initial capacity estimates, 1996
  Bell Labs prototype, 1998
Commercialization in LANs
  Began study in 2003.
  First appeared in 802.11n 2009
Commercialization in cellular:
  4G systems, approximately 2004
  5G systems: Integral component for support for mmWave

## Slide 7: MIMO Narrowband Capacity
Consider narrowband MIMO channel from previous lecture:
  Channel matrix
  : signals to the TX antennas
TX power constraint:
  Total energy constraint on all antennas
This section: make two critical assumption:
  TX and RX knows and exactly (called CSI-T and CSI-R)
  We will relax these later
RX array
TX array

## Slide 8: Applying Transforms with the SVD
Take reduced SVD of the channel:
TX and RX apply transforms
  TX transform: (also called a pre-coder)
  RX transform:
Theorem: The channel from to is diagonal:
Creates independent channels:
TX transform
RX transform
=

## Slide 9: Proof of the Diagonalization
Consider channel from to :
Noise:
  Since and , is also Gaussian
Hence, transforms diagonalize the channel:
=

## Slide 10: Virtual Channels
Diagonalizing the channel creates virtual channels
Number of virtual channels =
  = Number of orthogonal paths in the environments
Correspond loosely to the physical paths
  Suppose spatial signature of each physical path is orthogonal
  In this case, directions of virtual channel = direction of physical path
=
TX array
RX array

## Slide 11: Shannon Capacity
With diagonalizing transform:
Assume TX allocates power uniformly across all virtual channels
  Each channel gets energy per symbol
  This is not optimal. We will look at improved allocations laer
Total capacity (bits per degree of freedom)
  eigenvalues of eigenvalues of
  SNR on virtual path

## Slide 12: Log-Det Form of the Shannon Capacity
The Shannon capacity is commonly written in an alternate form:
Proof:
  Take eigenvalue decomposition:
  Let
  Hence
  But this is the capacity from the previous slide

## Slide 13: SNR Per Antenna
To understand benefit of spatial multiplexing, compare to a SISO system
Channel from TX to RX has SNR
Definition: The SNR per antenna is the average single antenna SNRs:
  “Frobenius” norm of

## Slide 14: Frobenius Norm=Sum of Eigenvalues
Key property: The Frobenius norm where eigenvalues of
Proof:
  Diagonal entries of :
  Hence, “Trace” = sum of diagonals
  Property of trace:
  Take digonalization:
  Therefore:
Hence, SNR per antenna is sum of SNR per virtual path divided by

## Slide 15: SNR Per Antenna and Physical Path SNRs
Consider channel with paths
Assume:
  Phases are uniform in since they vary with time and frequency
  and (spatial signatures only include phase rotations)
  Element gains are included in the complex gains
Each physical path has an SNR per antenna of
Theorem: Taking average over phases
Conclusion: SNR per antenna = sum of SNRs of each physical path per antenna

## Slide 16: Virtual Path SNRs and Path SNRs
Consider channel with paths
Assume paths are orthogonal and normalized such that
  and
  This will occur when the paths arrive and depart in orthogonal directions
Theorem: Under the above normalization assumptions, there will be virtual paths with SNR
Proof: From Unit 8, we saw the eigenvalues of are .
  Hence, the virtual path SNR is
Conclusion: For orthogonal directions, MIMO provides an SNR gain of on each path

## Slide 17: Coding Architectures
Spatial multiplexing creates virtual channels
  Each channel has SNR
Two possible transmission methods
Single codeword:
  Encode bits for symbols into one codeword
  Codewords sees varying SNR across symbols
  Adjust MCS for ergodic capacity
Multiple codewords:
  Divide bits into streams
  In each stream, encode bits for symbols into a codeword
  Each codewords sees a constant SNR
  Set MCS for each codeword to match SNR
Encoder
SNR
SNR
Decoder
Single Codeword
Encoder
SNR
SNR
Decoder
Multiple codewords

## Slide 18: Capacity with Practical Codes
Shannon capacity is
  Bits per channel use
  Can be achieved with optimal single or multiple codeword method
To account for practical codes, usually assume a model:
  Max spectral efficiency, based on modulation
  bandwidth loss
  SNR loss
Typical values for cellular systems:
SNR
SNR

## Slide 19: Examples
We will illustrate the calculations in this unit in two cases
Parameter | High-Dim Array | Low-Dim Array | Remark
Carrier | 28 GHz | 2.3 GHz | 
TX Array | 4x4 URA | 4x1 ULA | Typical gNB
RX Array | 8x1 ULA | 4x1 ULA | Typical UE
Num paths | 20 |  | 
Relative path gains | Exponential, Mean = 10 dB |  | 
AoA Az | Unif[-60,60] | Unif[-180,180] | Low-dim case has rich scattering
AoD Az | Unif[-30,30] | Unif[-180,180] | 
AoA and AoD El | Unif[-20,20] | Unif[-20,20] | 
Parameter | High-Dim Array | Low-Dim Array | Remark
 | 28 GHz | 2.3 GHz | 
TX Array | 4x4 URA | 4x1 ULA | Typical gNB
RX Array | 8x1 ULA | 4x1 ULA | Typical UE
Num paths | 20 |  | 
Relative path gains | Exponential, Mean = 10 dB |  | 
AoA Az | Unif[-60,60] | Unif[-180,180] | Low-dim case has rich scattering
AoD Az | Unif[-30,30] | Unif[-180,180] | 
AoA and AoD El | Unif[-20,20] | Unif[-20,20] | 

## Slide 20: Eigenvalue Distribution
Plot: SNR per virtual path
  Channel matrix normalized to SNR per antenna = 0 dB
  Max gain in any one path is
Low-dim case
  Up to 4 paths
  Eigenvalues evenly spread due to rich scattering
High-dim case
  Up to 8 paths
  Eigenvalues concentrated in a few dominant paths
High-dim array
Low-dim array

## Slide 21: Rate vs SNR
For each SNR per antenna:
  Rescale channel matrix
  Compute rate assuming uniform distribution across all streams
  Assume rate per stream:
Also plotted:
  SISO rate with SNR per antenna
See significant possible gain
  But not a fair comparison
  Should compare against beamforming
High-dim array

## Slide 22: Outline
Spatial Multiplexing with CSI-T and CSI-R
Power Allocation and Rank Selection
Spatial Multiplexing with CSI-R Only
Channel Estimation and CSI-R
CSI-T Feedback and Statistical Pre-Coding

## Slide 23: Spatial Multiplexing vs Beamforming
Beamforming:
  Places all energy on virtual path with strongest SNR
  Achieves rate
  If codes achieve capacity,
Spatial multiplexing:
  Transmit energy evenly on virtual paths
To compare, consider two extreme cases:
  Equal SNRs for all
  Single dominant SNR
SNR
SNR
SNR

## Slide 24: Spatial Multiplexing vs Beamforming Equal SNR streams
First, suppose all virtual directions have same power
  BF rate:
  Spatial mux rate
Low SNR regime (power limited)
  No gain
High SNR regime (bandwidth limited)
  . Gain of .
  Spatial multiplexing adds degrees of freedom
Spatial multiplexing is like adding bandwidth
Simulation:
streams
4.5 bps/Hz
4.5 bps/Hz

## Slide 25: Spatial Multiplexing vs Beamforming Single Dominant Stream
Now suppose that there is a single dominant virtual direction
  for
BF rate:
Spatial mux rate
Spatial multiplexing with uniform power allocation is worse!
  Waste energy in directions with no SNR

## Slide 26: Power Optimization and Water-Filling
We can allocate the power optimally
Let fraction of power allocated to stream
Optimize the rate:
Some special cases:
  Beamforming: Place all power in best stream: for
  Uniform power allocation:
When optimal solution is given by “water-filling” (see text)
  Constant set to satisfy constraint that
  Allocate energy inversely proportional to SNR
  Some streams are allocated zero energy

## Slide 27: Power Allocation
Consider sub-optimal strategy
  Uniformly allocate to top streams
Plot to the right:
  Synthetic channel from before
  We see that (BF) optimal at lower SNRs
  At higher SNRs, multi-streams become useful

## Slide 28: Optimal Rank Selection
Water Filling is difficult for a general rate function
Consider sub-optimal strategy
  Uniformly allocate to top streams
Left plot:
  Best rate among all possible ranks
Right plot:
  Best rank
We see rank increases with SNR
Optimal rate
Optimal rank

## Slide 29: Water-Filling
Assume the rate per stream is given by Shannon’s formula:
Maximize s.t.
  SNR on virtual stream if all power is allocated to stream
Take Lagrangian:
Take derivative:
For positive streams:

## Slide 30: Example: Water-Filling vs Rank Selection
Compare two strategies:
Water-filling: Optimal allocation
Rank selection:
  Uniform power among best directions
Comparison:
  Gain from waterfilling is small
  Only helps at very high SNR

## Slide 31: Outline
Spatial Multiplexing with CSI-T and CSI-R
Power Allocation and Rank Selection
Spatial Multiplexing with CSI-R Only
Channel Estimation and CSI-R
CSI-T Feedback and Statistical Pre-Coding

## Slide 32: Challenges in Obtaining CSI
Above analysis assumes TX and RX have CSI
CSI-R: RX knows
  Generally possible with sufficient reference signals
  Reference signals add overhead
  Overhead is reasonable if number of streams coherence time
CSI-T: TX knows
  Requires feedback from RX or measurements in reverse direction
  With small-scale fading, changes rapidly
  Instantaneous is generally difficult
Later, we will discuss how to obtain both
This section: Understand effect of lacking CSI-T
CSI-R
RX knows
CSI-T
TX knows

## Slide 33: Problems in Lacking CSI-T
We will see that lacking CSI-T causes two problems
TX power mis-allocation
  TX does not know virtual path directions
  TX may send data into directions with poor SNR
  Wastes TX energy
Inter-stream interference
  Streams end up “mixed” at RX (Each depends on multiple )
  RX must separate the streams
  Can be mitigated with equalization or joint decoding
  But equalization or joint decoding adds complexity and may incur a penalty loss
CSI-R
RX knows
CSI-T
TX knows

## Slide 34: Information Theoretic Formulation
Consider transmission over multiple symbols:
  Block length
TX encodes messages, bits per symbol
  Denote messages
Transmission energy assumption:
  Assumes TX energy is uniform over all antennas
  We assume this since the TX does not know the optimal direction
  We will see this loss can be significant
RX can perform any decoding. No computational limits
  For example, optimal decoding

## Slide 35: Information Theoretic Capacity
Information theoretic model:
  TX power constraint:
Theorem [Teletar,~2003]: Under optimal decoding with the block length the capacity is:

## Slide 36: Proof of the Teletar’s Result
Channel model:
From Shannon’s Theorem, capacity is
  Max is over distributions on
Fact 1: For any Gaussian entropy is
Fact 2: For with entropy is bounded
Given ,
If then
Hence
Capacity is
Get by using Gaussian distribution

## Slide 37: Comparison to CSI-T Case
We saw that if TX allocates energy TX power uniformly on all virtual directions, capacity is
Capacity with TX uniformly on all TX antennas is:
Conclusion: With optimal decoding:
  Can obtain capacity identical to TX uniformly on directions
There is a TX power mis-allocation loss:
  Loss of in SNR when . This is especially large when
  No water-filling. Hence, within the rank virtual streams, power is not allocated optimally

## Slide 38: TX Mis-Allocation Loss Example Low Dimensional Array Case
Simulation:
  Random channel with rich scattering
  AoA and AoD uniform on
TX mis-allocation loss is minimal
With rich scattering and small num antennas:
  All directions have good SNR
  Uniform power allocation is optimal

## Slide 39: TX Mis-Allocation Loss Example High Dimensional Array Case
Simulation from before:
  Random channel
Max rank is
At high SNR, the loss is
At lower SNRs, the loss is larger
  Wastes significant energy on poor rank directions

## Slide 40: Loss from Inter-Stream Interference
Prior capacity result required optimal decoding:
  Search over all possible codewords
Computationally impossible for even moderate block size
We consider a simple linear equalization scheme:
  Linear equalization followed by symbol demodulation and channel decoding
This method introduces a second loss due to inter-stream interference

## Slide 41: Linear Equalization Concept
Most practical systems use linear spatial equalization
  Perform linear transform to approximately invert and recover
  Followed by symbol demodulation on the symbols to create LLRs
  LLRs then used by the channel decoder
In contrast, we call the optimal decoder the joint decoding
  Since it jointly performs the symbol demodulation and channel decoding
Symbol demod
Channel decoder
LLRs
Spatial EQ

## Slide 42: Linear Zero-Forcing Equalizer
Estimate via a least-squares optimization
Solution is called the zero-forcing equalizer:
  The reason for the name will be clear later
Note for the inverse to exist we need
  More specifically, we need

## Slide 43: Zero-Forcing Equalizer Analysis
Suppose we use ZF equalizer
Then channel from to is
Creates parallel channels
Noise covariance matrix is:
SNR on each channel: Since

## Slide 44: Problems with Zero Forcing
SNR on each stream with zero forcing is:
For inverse to exist, requires that
Also, when eigenvalues of are small, will blow up
What is the optimal linear transform?

## Slide 45: Linear MMSE Equalization
Narrowband channel
Assume
  Assume and
  TX energy is in each antenna
  Select to minimize average error:
Optimal linear estimator from probability theory is

## Slide 46: Linear Equalizer: Interference + Noise
Narrowband channel
Equalized symbols:
  For now, consider general linear equalizer
Hence: and hence, per component
LMMSE receiver: Decode from treating inter-stream interference as noise
Desired signal
Inter-stream interference
Noise

## Slide 47: LMMSE: SINR
From previous slide:
On channel :
  Signal energy
  Interference energy:
  Noise energy:
SINR on channel

## Slide 48: LMMSE SINR
Channel ,
Consider linear equalizer
Theorem:
  With the LMMSE equalizer, , SINR per channel is:
  For any other linear transform ,
Proof: Follows from long linear algebra.
  See text

## Slide 49: LMMSE vs. ZF
At high SNR, LMMSE ZF:
  Recall
  If is invertible, as
For ZF, there is no inter-stream interference:
  Recall
  With
  Thus, for
  Hence, ZF forces the inter-stream interference to zero. Hence, the name
  But ZF amplifies the noise term
  Linear MMSE optimally trades off noise and inter-stream interference

## Slide 50: LMMSE vs. Joint Decoding
We saw that with optimal joint decoding capacity is:
With LMMSE, capacity is:
Fact:
Proof:
  Linear algebra fact: for any matrix ,
  This fact follows from a Cholesky factorization
  Therefore,

## Slide 51: LMMSE Loss: Low-Dim Case
Consider the low-dimensional example
  4 x 4 MIMO with rich scattering
  See parameters above
At low SNRs:
  LMMSE performs close to Joint decoding
  LMMSE performs much better than ZF
At high SNRs:
  Joint decoding provides a small advantage
  Gain of ~2 dB
  ZF performs close to LMMSE

## Slide 52: LMMSE Loss: High-Dim Case
Next consider the low-dimensional example
  and
  See parameters above
Linear equalization requires that
  channel rank = number of virtual directions with significant SNR
  Otherwise, cannot recover
When , we need to perform pre-coding:
  Estimate the number, of TX streams to use (somehow)
  Pre-code where is dimensional
At the receiver perform decoding on pre-coded channel
Pre-coder

## Slide 53: LMMSE Loss: High-Dim Case
We have and
Hence, some pre-coding is needed to use LMMSE
As an example, suppose we use random pre-coding
  Select streams (num of significant evals)
  Take a = random orthogonal methods
After random pre-coding:
  There is a significant loss.
  Even with optimal joint decoding
  LMMSE and ZF have further losses
For high-dim arrays, some CSI-T is needed
  This is particularly important in mmWave
  Need to intelligently select directions

## Slide 54: Improving over LMMSE
We see that LMMSE decoding is not optimal
Incurs a penalty due to inter-stream interference
Several possible advanced receivers can be used to reduce inter-stream interference:
LMMSE + SIC:
  Successively decode each stream and cancel it out
  We describe this next
Turbo / joint decoding methods:
  Iteratively perform iterations of the decoder with the LMMSE
  Take the soft information of decoder to improve the LMMSE
  See text

## Slide 55: LMMSE + SIC: Transmitter
TX:
  Divide data into streams
  Get information bits
  Encode codewords
  Modulate to create symbols
  TX on TX antenna
Channel:
  Can be written:
Encoders

## Slide 56: LMMSE + SIC: First Stream
Decode stream 1:
  Perform LMMSE estimate of from to get
  Signal will have interference from
  Treat signals from as noise
  Decode bits from LMMSE signal (symbol demod + decoder)
Cancellation phase
  Re-encode estimated bits
  Subtract out to give
  If
  Residual signal has no contribution from
Encoders
LMMSE estimators
Decoders

## Slide 57: LMMSE + SIC: Subsequent Streams
For stream 2:
  As stream 1, get LMMSE estimate of
  LMMSE uses residual
  Residual has no contribution from
  Interference is only
  Treat signals from as noise
  Decode bits , re-encode and subtract
Continue for all streams
Encoders
LMMSE estimators
Decoders
Re-encoders

## Slide 58: LMMSE + SIC Performance
Theorem: The capacity of the LMMSE SIC scheme is equal to optimal joint decoding
Proof: Use linear algebra to estimate SINR in each stream.
  With some linear algebra manipulations, you can show you end up at the same capacity
Conclusions: LMMSE + SIC is a practical method to get optimal joint decoding
Computational issues:
  Error propagation: If one stream is in error, you cannot subtract
  Difficult to merge with H-ARQ.
  Need large buffer for symbols. This buffer is the main bottleneck in practical systems
Commercial systems:
  Have generally only used LMMSE+SIC on small numbers of antennas
  LMMSE without SIC is overwhelmingly dominant implementation method

## Slide 59: Outline
Spatial Multiplexing with CSI-T and CSI-R
Power Allocation and Rank Selection
Spatial Multiplexing with CSI-R Only
Channel Estimation and CSI-R
CSI-T Feedback and Statistical Pre-Coding

## Slide 60: Obtaining CSI-R
Assume TX has selected a pre-coder
RX sees channel
Results in a channel matrix
  = number of streams
  = number of RX antennas
For CSI-R, RX needs to estimate
  RX does not need to know the pre-coder or the true channel!

## Slide 61: Reference Signals
Most systems use some form of reference signals
One set of reference signals for each TX stream
  Typically allocated on orthogonal resources
Example to right: One sub-frame in LTE
  Configuration for 4 TX “ports”
  Resource elements to are the RS for each port
  Each port has 2 to 4 REs per resource block
In a RS for stream , we get a measurement:
  Estimate th column of

## Slide 62: Example: 5G NR DM-RS
DM-RS: Demodulation reference signals
  Reference signals contained in downlink data
  Shown in yellow squares
Multiple layers in 5G:
  Each spatial layer is modulated to a “port”
  One set of reference signal for each port
  Reference signals are different ports are orthogonal
  Bottom right: RS for 8 port transmission
  Each RS allocated on 12 REs
  Each RE shared with 4 other ports
  Uses an orthogonal covering code (OCC)

## Slide 63: Overhead Issues
Suppose channel is constant over symbols
  coherence bandwidth, coherence bandwidth
We need at least one reference symbol per transmitted stream in each coherence block
Overhead is , number of RS = number of streams
Rate will be:
  Training loss:
  Power loss per stream:
  Bandwidth increase: Sum over
In general, there is a tradeoff

## Slide 64: Information Theoretic Calculation
Hochwald and Hassibi, 2003
Simplified block fading model
  Channel is constant over uses
  Allocates RS in each block
With known channel
  Increasing num TX streams helps
Without non-coherent channel
  Eventually hurts
  Spend more energy on training
  Less energy on data

## Slide 65: Outline
Spatial Multiplexing with CSI-T and CSI-R
Power Allocation and Rank Selection
Spatial Multiplexing with CSI-R Only
Channel Estimation and CSI-R
CSI-T Feedback and Statistical Pre-Coding

## Slide 66: Problems in Obtaining CSI-T
Channel state information is asymmetric
Receiver:
  Can directly measure the channel
Transmitter:
  No direct measurement
We discuss two possible methods:
  Precoding matrix feedback
  Reverse link reference signal with reciprocity
RX
TX

## Slide 67: Pre-coding Feedback
Feedback method
  TX sends CSI reference signals from each antenna
  RX measures complex channel matrix
  RX computes optimal TX pre-coding matrix
  Also determines optimal rank
  RX sends TX pre-coder back to TX
  Pre-coder Matrix Indicator (PMI)
  TX uses pre-coder in transmission
Problem:
  Must feedback within time coherence
  Many need to send freq-dependent pre-coders
  Potentially high overhead for fast varying channels
CSI-RS
PMI
Estimate
Compute TX pre-coder and rank
TX pre-codes with
RX processing
Pre-coded data
TX
RX

## Slide 68: Statistical Pre-Coding
Consider channel:
Parameters vary in two different time scales:
  Small-scale variations: vary with time and frequency. Difficult to track
  Large-scale variations: and and vary with path gains. Slower varying. Easier to track
Statistical pre-coding concept:
  Measure on many different time and frequencies
  Assume varies but large-scale parameters are constant
  Based TX pre-coding on statistics of
  Also called long-term pre-coding
TX array
RX array

## Slide 69: TX and RX Spatial Covariance Matrices
Statistical pre-coding is typically based on the spatial covariance matrices
Consider channel:
Define TX and RX spatial covariance matrices
  Average is over small-scale parameters
If phases are i.i.d. :

## Slide 70: Statistical Pre-Coding with
Estimate
  Measured over many time and frequency instances
Take eigenvalue decomposition:
  Assume sorted
To transmit on streams:
  Take TX pre-coder: corresponding to largest eigenvalues
  Use pre-coding

## Slide 71: Instantaneous vs. Statistical Pre-Coding
Statistical pre-coding:
  Select one : Maps streams to antennas
  On each channel realization, see channel matrix:
  Obtain ergodic capacity:
Instantaneous pre-coding:
  Can select pre-coder for each channel realization
  Get ergodic capacity:

## Slide 72: Example
High-dim array case:
  Transmission rank and
  Instantaneous selects best directions in each realization. Statistical select directions from
  Uniform power allocation across all
Rank=4
Rank=8