## Slide 1: Unit 3. Multi-Path Fading
Ece-gy 6023. Wireless communications
Prof. Sundeep rangan

## Slide 2: Fading
From the Introduction of a classic text:
There are two fundamental aspects of wireless communication that make the problem challenging and interesting.
…First is the phenomenon of fading … …Second …there is significant interference …

## Slide 3: Learning Objectives
Describe up and down-conversion in time- and frequency-domain
Describe the steps in the DAC and ADC including the filtering
Compute a discrete-time and continuous-time base equivalent channels from the passband
Simulate fractional delays and gains in the sampled data
Describe and simulate a deterministic multi-path wireless channel
Compute the time-varying frequency response given the path parameters
Describe a statistical model for multi-path fading
Approximately compute the coherence time and bandwidth given a channel

## Slide 4: Outline
Review of Up- and Downconversion
Review of TX and RX Sampling
Doppler and Multi-Path Fading
Statistical Descriptions of Fading

## Slide 5: Up- and Downconversion
RF communication systems:
  Information occurs and is processed in complex baseband
  Transmitted and received in real passband
Up and down-conversion: Shift center frequency of signals
Also called mixing
upconversion
downconversion
0
f
-
Complex baseband
f
0
Real passband

## Slide 6: Up and Down-Conversion in Time Domain
Complex baseband:
  Two real signals,
  Or one complex signal:
upconversion
downconversion
Real passband:
Note: downconversion needs:
Multiplication by 2
Low pass filtering

## Slide 7: Mixing in Frequency Domain
Baseband signals
  Centered around complex
  single sided bandwidth
  two sided bandwidth
  Band-limited to
Passband signals
  Centered around real
  bandwidth (per side or image)
  Band-limited to
0
A
0
A/2

## Slide 8: Discrete IQ Mixer
LO = “local oscillator” = square or sine wave at
I1, I2 = I and Q inputs.
  Generally, lowpass
RF = passband output centered at
Datasheet | RF [GHz] | LO [GHz] | IF [MHz] | Conversion Loss [dB] | Image Rejection [dB] | Amplitude Deviation [dB] | Phase Deviation [Degrees] | Isolations L-R [dB] | Isolations L-I [dB]
IQ-0318 | 3 to 18 | 3 to 18 | DC to 500 | 7 | 22 | 0.75 | 10 | 40 | 20
http://www.markimicrowave.com/Mixers/IQ_Quadrature-IF_Double-Balanced/IQ-0318.aspx

## Slide 9: Baseband Equivalent Channel
Filtering at passband equivalent to complex baseband filter
Assuming downconversion filter is ideal:
  Simply shift to the left by .
Upconvert
Downconvert
Filter
Filter
=

## Slide 10: Important Special Case: Delay
Delay, gain in passband delay, gain and phase rotation in baseband
Proof:
  Passband frequency response is:
  Baseband frequency response:
  Equivalent impulse response:
Passband channel
gain delay
Baseband equivalent channel
gain delay
= phase rotation

## Slide 11: Synchronization and Delay Errors
Time synchronization at the receiver:
  Estimate the arrival time of the signal
  Starts processing remainder of signal starting at
  Equivalent to shifting received signal ahead in time by :
  Remaining time error:
Later, we will discuss:
  How to estimate (synchronization) and how to correct for gain and phase error (equalization)
Delay & gain
0
Delay estimate
Shift
Sync

## Slide 12: Frequency Errors
Oscillators at TX and RX always have some mismatch. To analyze, suppose:
  Upconversion:
  Downcoversion: )
LO error leads to time-varying gain:
  Frequency and phase shift
LO 1
LO 2

## Slide 13: In-Class Problems

## Slide 14: Outline
Review of Up- and Downconversion
Review of TX and RX Sampling
Doppler and Multi-Path Fading
Statistical Descriptions of Fading

## Slide 15: Typical Digital Communication Path
All modern communication systems TX and RX digital samples
Transmitter: DAC + filtering with . Filtering used to:
  Suppress out of band emissions
Receiver: Filters with then performs ADC. Filtering plays two roles:
  Reduces noise
  Remove out-of-band signals before ADC. (i.e. Anti-aliasing)
Filter design discussed in digital communications class
Ideal A/D
Ideal D/A
TX samples
RX samples

## Slide 16: Review of DTFT
Given discrete-time sequence
  Real or complex
Discrete-time Fourier Transform:
Inverse DTFT:
Note is always a periodic signal
  Can take integral for inverse DTFT on any period of
is the discrete frequency. Units is radians per sample.
For finite length signals and finite number of , can be computed via FFT
Review in your signals and systems class

## Slide 17: Common DTFT Pairs
See Wikipedia

## Slide 18: Discrete-Time Systems
Consider discrete-time LTI system
Time-domain: Characterized by impulse response
Frequency-domain: Characterized by frequency response

## Slide 19: DT Equivalent Channel
Discrete-time baseband equivalent channel:
  Describes equivalent mapping from to
  Includes effects of TX and RX filtering and continuous-time baseband channel
Band-limited filters:
  Suppose one of is bandlimited to (no out-of-band emissions or aliasing)
  Then, discrete-time equivalent channel reduces to:
ADC
DAC
=

## Slide 20: Ideal Filtering
Suppose sample rate
“Ideal” TX and RX filter :
  In frequency domain:
  Also called “brick wall” filter
Most practical filters match this well
  Up to gain and delay
ADC
DAC
=

## Slide 21: Ideal Filtering
Assume TX and RX filters are ideal
Theorem: DT equivalent channel is the re-scaled continuous-time channel
  Frequency mapped to
ADC
DAC
=

## Slide 22: Special Case: Delay
Suppose passband has a gain and delay.
Then discrete-time frequency-domain: gain and linear phase rotation over frequency
  Rotates radians every period
In discrete-time time-domain: gain, constant phase rotation and sinc filter with delay
 | Passband | Continuous-Time Baseband | Discrete-Time Baseband
Impulse response |  |  | 
Frequency response |  |  | 
 | Passband | Continuous-Time Baseband | Discrete-Time Baseband
Impulse response |  |  | 
Frequency response |  |  | 

## Slide 23: Sinc Filter with Integer Delays
Suppose we have ideal filtering and passband has delay and gain
From previous slide,
Special case 1: No delay
  Baseband channel introduces only gain
Special case 2: Integer delays
  Baseband channel introduces gain and integer shift
Ex: Suppose sample rate is 20 MHz and signal is delayed by 400 ns.
  Integer delay in discrete-time signal is samples

## Slide 24: Sinc Pulses with Fractional Delay
Causes blurring over multiple samples
Inter-symbol interference
Will need equalization to correct
  More on this later

## Slide 25: Simulating Fractional Delays in MATLAB
Code on previous slide was create with DSP toolbox
Creates T x D matrix
Row is delayed by

## Slide 26: In-Class Problem: Fractional Delays on Constellations

## Slide 27: Outline
Review of Up- and Downconversion
Review of TX and RX Sampling
Doppler and Multi-Path Fading
Statistical Descriptions of Fading

## Slide 28: Receiver with Local Motion
With the RX in motion, the propagation delay changes with time.
In complex baseband signal:
Local motion assumption: for small
  Effect of the change in propagation delay is only in the complex exponential
Then:
Mobile velocity

## Slide 29: Doppler Shift
Single path with local motion:
  Complex gain:
  Doppler shift:
  Delay:
For a single path: Local motion causes a phase rotation, but no change in amplitude
Mobile velocity

## Slide 30: Example: Computing Doppler Shift
Suppose: carrier frequency is =2.1GHz Car moves towards a base station at 100 km/h.
What is the Doppler shift?
Answer: =100km/h= m/s, c= m/s,
If the angle away from BS at
=100 km/h

## Slide 31: Multi-Path Models
Most channel consists of many paths
  Direct paths
  Reflections, transmissions, diffraction, …
  LOS and NLOS paths
Wideband time-domain baseband model:
  : Complex path gain
  : Doppler shift of path
  : Delay of the path

## Slide 32: Time-Varying Frequency Response
Multipath channel:
Consider exponential input:
Output is:
Time-varying frequency response
May also write:

## Slide 33: Example with Two Paths
To simplify understanding, consider two path model
Time-varying response:
Power gain:

## Slide 34: Variation in Time
Plot shows =10 Hz, ,
Fixed frequency
Look at time variations
Rate of variation depends on Doppler spread:
Size of variation depends on spread of gains:
  Avg:
  Min: : Destructive interference
  Max: : : Constructive interference
With equal path gains, there are nulls

## Slide 35: Variation in Frequency
Fixed frequency
Look at time variations
Period of variation depends on delay spread:
Size of variation depends on spread of gains:
  Avg:
  Min:
  Max:
Plot shows ns, ,

## Slide 36: Fading
Over time and frequency, paths can either
  Constructively interfere Peaks
  Destructively interfere Nulls
Process is called fading
  Intermittent channel quality
One of the most significant challenges in wireless
Later, we will discuss how to overcome fading

## Slide 37: Narrowband Approximation
Multi-path channel:
Define delay spread:
  Max path difference in seconds
Narrowband approximation: is band-limited to then
  Proof below
  Coherence bandwidth
Effective single path gain: :
  Channel appears as a single path channel with time-varying gain
  Channel gain is band-limited to max Doppler

## Slide 38: Example: 3GPP Cluster Delay Line Model
3GPP has several deterministic multi-path models
Called Cluster-Delay Line (CDL)
Can be downloaded in MATLAB 5G Toolbox
  Gives the gain, delay and angles of each path
  This ex: CDL-C with 24 paths
Path delay profile
Path AoA azimith profile

## Slide 39: Computing the Doppler of Each Path
Computing the Doppler shift of each path
  Suppose that RX has velocity vector
  Doppler shift of path is:
In this simulation: m/s in x-axis
RX velocity
Direction of arrival vector

## Slide 40: Computing the Narrowband Response
Narrowband response
Plot at and 1 MHz
Max Doppler Hz
  See fast variation on order ms
Can see deep fades

## Slide 41: Narrowband Approximation Proof
Want to show: If band-limited to then
Prove this for . Other frequencies are similar.
Thus, is bandlimited to .
Therefore,
In particular since
Hence:

## Slide 42: Examples: When is Narrowband Valid?
Bluetooth
  Bluetooth hops over channels of bandwidth 1 MHz each.
  Indoor delay spread typically ns
  Coherence bandwidth MHz B
  Narrowband approximation valid
LTE outdoor cellular system
  A typical channel is 20 MHz
  Outdoor delay spread
  Coherence bandwidth MHz B
  Narrowband approximation not valid

## Slide 43: OFDM Time-Frequency Grid
OFDM modulation: Widely-used method
  4G and 5G cellular systems
  Many 802.11 standards
Divide channel into sub-carriers and OFDM symbols
  Resource element: One time-frequency point
Data is transmitted is an array:
  OFDM symbol index
  = subcarrier index
  One complex value per RE.
  Called a modulation symbol
See digital communication class
  We will also review again when we discuss equalization
Subcarrier spacing
OFDM symbol
Time
Frequency

## Slide 44: OFDM Channel with Fading
OFDM channel acts as multiplication: Under normal operation (delay spread is contained in CP):
OFDM channel gains can be computed from the multi-path components
  OFDM symbol time, sub-carrier spacing
  For each path: Doppler shift, Delay, phase of path, path received energy
RX symbols
Channel
TX symbols

## Slide 45: Summary
Single path with no motion:
  Delay and constant phase shift
Local motion in single path causes Doppler
  A time-varying phase rotation
  But channel gain is constant
Multiple paths causes fading
  Constructive and destructive interference of paths
  Variation in gain over time
Described by a time-varying frequency response
  Variations is time due to Doppler spread
  Variations in frequency due to delay spread

## Slide 46: In-Class Exercise: OFDM Channel Response

## Slide 47: Outline
Review of Up- and Downconversion
Review of TX and RX Sampling
Doppler and Multi-Path Fading
Statistical Descriptions of Fading

## Slide 48: Statistical Model
Fading depends on the multipath distribution
Multipath is site-specific
Statistical model:
  Describes a probability distribution of channels
  Trained on an ensemble of channels in some environment
Used in evaluation of communication system
Example questions:
  How well does a system do on average?
  What is the probability that I will obtain sufficient coverage?

## Slide 49: Random Path Statistical Model
RX signal has many random, independent paths
Time-varying frequency response:
  Assume ) i.i.d.
  Path gains: are zero mean and
As , is a complex Gaussian,
  Follows from Central Limit Theorem
  Independent real and imaginary components
  : Average power gain
  Variance for real and imaginary components
Direction of motion

## Slide 50: Rayleigh Distribution
Rayleigh fading: Channel response is
Let magnitude
  Represents amplitude gain
Has Rayleigh distribution:
  PDF:
  CDF:
  Mean:
  Second moment:
Probability distribution
https://en.wikipedia.org/wiki/Rayleigh_distribution

## Slide 51: Exponential Distribution
Consider Rayleigh fading complex gain
Magnitude is Rayleigh
Instantaneous gain has exponential distribution
  Average gain is
For channel, represent power gain (in linear scale)
PDF for

## Slide 52: Example Calculation
Suppose the channel experiences Rayleigh fading.
What is probability gain will be 15 dB below the average?
  Called a 15 dB fade.
Answer:
  Gain is 15 dB below average when
  From exponential distribution:
  For small ,
  For 15 dB fade,

## Slide 53: Doppler Spectra
Consider statistical model:
  Paths are i.i.d. and are zero mean,
  Assume is large
For a given , complex gain
As varies , is a Gaussian random process
Auto-correlation:
  Describes how correlated the process is over time and frequency
  Depends on the distribution of angles and delays

## Slide 54: Jakes Model
At a fixed frequency :
Complex Gaussian process
Statistics depend on angular distribution
Jakes model:
  Angles uniform from
Asymmetric Jakes:
  uniform
Angular spread:
  Arises from diffuse reflection
Jakes
Angles unif
Asym Jakes
Asym Jakes
Gain (dB)
Angle (rads)

## Slide 55: Fading Models in MATLAB
Comm Toolbox:
  Efficient, general fading models
Create a comm.RayleighChannel object
Run the channel to get:
  Output and gain

## Slide 56: Auto-Correlation
Fix a frequency and consider auto-correlation over time:
  Expectation is over angle
  Depends on distribution of
Plot: for uniform in
  Computed numerically in MATLAB (see demo)
  Plotted vs normalized delay
  For Jakes spectra
  Uncorrelated at
As angular distribution is smaller:
  Correlation is higher with delay
  Highly directional channel vary slower

## Slide 57: Computing Auto-Correlation Numerically
Correlation in previous slide
  Expectation is over angle
Generally, no analytic solution
Compute via numerical integration
  See demo

## Slide 58: Coherence Time and Frequency
Consider time varying frequency response
Coherence time:
  Max interval where
  How fast channel changes in time
  Related to Doppler spread
Coherence bandwidth
  Max interval where
  How fast channel changes in frequency
  Related to delay spread
Critical for many procedures:
  Channel estimation, tracking, coding, ARQ, …
  More on this later
Realization of a Jakes process with 1/fmax = 0.1 sec

## Slide 59: Winner-3GPP-Spatial Cluster Model
Paths arrive in clusters.
Clusters have subpaths (also called rays)
Each cluster has:
  Center angle and a statistical model for the delay and angular spread
From 3GPP SCM-132

## Slide 60: Fading at Different Time Scales
From Goldsmith, “Wireless Communications”
Three mechanisms for path loss variations
Distance-based path loss
Shadowing
Small-scale multi-path fading
Slower
Faster

## Slide 61: Fading at Different Scales Models
Source of variation | Mathematical model | Typical spatial coherence | Typical temporal coherence
Small-scale fading from multi-path fading | Rayleigh or Rician distribution | ~ 1 wavelength | 15 ms (v=10m/s, fc=2GHz)
Large-scale fading from variations in shadowing | Lognormal distribution | 10 to 100 m | 1 to 10 sec
Path loss variations | Path loss exponent | 100 m or larger | 10 sec
Different fading processes and variations occur at much different time / space scales
Methods to combat these are different