## Slide 1: Unit 7. Channel Estimation and Equalization
Ece-gy 6023. Wireless communications
Prof. Sundeep rangan

## Slide 2: Learning Objectives
Describe role of channel estimation in the receiver steps
Configure reference signals in OFDM
  Compute overhead
  Qualitatively relate density to the coherence time and bandwidth
Implement and simulate simple kernel-type channel estimators
Compute bias and variance of the kernel estimators
Optimize the kernel to minimize the bias + variance error
Compute the signal to distortion and noise ratio (SNDR) for a given estimator
Measure the SNDR via simulation
Implement a simple channel estimator and equalizer for 5G NR downlink

## Slide 3: Outline
Role of Channel Estimation and Equalization
OFDM Channel Estimation via Kernel Regression
Bias-Variance Tradeoff

## Slide 4: Channel Estimation and Equalization
Key challenge: Equalizers need a channel and/or noise estimate
Channels fade in time and frequency
  In OFDM, can be described by time-varying frequency response:
Equalizers: Estimate TX symbols from faded symbols
  Approximately invert the channel or MMSE
Fading channel
Equalization
h

## Slide 5: Reference Symbols
Equalizers require training or reference signals
TX sends a known reference sequence on some locations
RX sees
Estimates channel and/or equalizer for
Fading channel
Equalizer estimator
h
TX reference
RX reference

## Slide 6: Receiver Steps in OFDM
Sync & AGC
Data-Reference demux
OFDM FFT
Channel & noise estimate
Equalization
Demodulator
Decoder
Data symbols
Reference symbols
LLRs
Equalized symbols
This unit

## Slide 7: Frequency-Domain and Time-Domain EQ
Frequency-Domain Equalization:
  Typically, an OFDM channel
  Estimate frequency-domain channel
  Perform equalization with a filter
  Used in 4G, 5G OFDM systems, most 802.11 versions
Time-Domain Equalization:
  Model channel in time-domain
  Estimate channel impulse response
  Perform equalization with a filter
  Used in 2G, 3G CDMA systems, 802.11ad single carrier version
  Do not discuss in this unit (except next few slides)

## Slide 8: 802.11 ad Time-Domain Equalizer
STF: Short training field
  AGC, detection of packet
  coarse estimate of timing
  Process as previous lecture
CEF: Channel estimation field
  Train equalizer
  Apply equalizer
802.11ad uses time-domain equalization

## Slide 9: 802.11ad Preamble Details
Based on complementary Golay codes
Have low auto-correlation
Gsamp/S
For data packets: STF = 1.23 s, CE= 0.654 s
Control packets
Longer STF.
Need to be decoded by all stations. No directional gain
Data packets
Shorter STF

## Slide 10: Outline
Role of Channel Estimation and Equalization
OFDM Channel Estimation via Kernel Regression
Bias-Variance Tradeoff

## Slide 11: OFDM Channel Estimation
OFDM Channel
  Symbol and sub-carrier
Channel varies
  Over time due to Doppler spread
  Over frequency due to delay spread
Problem: Estimate
Estimate needed to demodulate data
51 RB, 15 kHz SCS, MHz bandwidth NR slot
500 ns delay spread, 200 Hz Doppler, AoA

## Slide 12: Reference Signals
OFDM Channel
5G NR Demodulation Reference Signals
  Called DM-RS
  Transmitted in downlink with data (PDCSH)
  Very configurable in terms of over-head
Basic channel estimation idea
  Transmit know on DM-RS.
  Estimate on DM-RS symbols
  Interpolate to data symbols

## Slide 13: Configuring in DM-RS
Example configuration
  DM-RS on one symbol in RB
  Occupies 6 out of 12 REs
Also added a phase-tracking reference signal
  Tracks phase variations over time
  Useful for carrier frequency offset and phase noise (more on this later)
Many configurations possible
See excellent MATLAB 5G tutorial with videos

## Slide 14: Configuring in MATLAB
MATLAB 5G Toolbox
  Provides all config possibilities
  Easy to use
See excellent MATLAB 5G tutorial with videos:

## Slide 15: Estimating Channel in a Single Symbol
First consider estimation in one symbol
True channel is
  sub-carrier index
RX:
DM-RS known
Example to right:
  10 MHz bandwidth
  200 ns delay spread
  10 dB SNR on DM-RS
Subcarrier

## Slide 16: Raw Channel Estimate
Channel:
On DM-RS positions, is known
Raw channel estimate:
  Can be computed in every DM-RS position
We see estimate is noisy

## Slide 17: Raw Channel Estimate Error
Channel: ,
  Drop sub-carrier index (since we are looking at one RE)
Raw channel estimate:
Error is
Relative error is:
  SNR on the symbol
Relative error is the inverse of the SNR

## Slide 18: Smoothing the Estimate
Raw channel estimates are:
  Noisy
  Only available on DM-RS locations
Often smooth the estimate
  Fit over all locations
Many options
  Linear interpolation, splines
  Parametric
We look at Kernel regression
  Works well
  Easy to implement and analyze

## Slide 19: Kernel Regression
Problem: Want to estimate
  Given noisy values
  At locations
Kernel function
  Example radial basis function:
  “Bandwidth”
Kernel estimate:
  Weights raw samples by the distance
Takeda, Farisu, Milanfar, Kernel Regression for Image Processing and Reconstruction, 2007

## Slide 20: Example
RBF Kernel
  Bandwidth
  Length on each side
Estimate is visibly smoother

## Slide 21: MATLAB Implementation
Easy to implement in software or hardware
See demo

## Slide 22: Extending the Estimate to Other Symbols
Up to now:
  Estimated at channel at a single OFDM symbol
  on OFDM symbol
Can be extended to other symbols in slot:
  Assumes channel is constant over time
  Coherence time Slot time
Can also have multiple RS symbols
  Useful when there is time variations in slot
See lab
Subcarrier
Channel estimate at

## Slide 23: In-Class Exercise

## Slide 24: Outline
Role of Channel Estimation and Equalization
OFDM Channel Estimation via Kernel Regression
Bias-Variance Tradeoff

## Slide 25: Mean Squared Error with Kernel Regression
Problem: True channel
  Given noisy values at sub-carriers .
Kernel estimate:
Mean-squared error:
  Measures the accuracy of the estimate
  For now, model as deterministic
  Average over noise
May also be interested in the normalized MSE:

## Slide 26: Bias and Variance Error
Error:
Since is linear in can write
  Signal component:
  Noise component:
MSE can be written as two components:
  Bias error:
  Variance error:

## Slide 27: Variance Error
Noise term
Recall
  noise on the reference signals, Reference signal energy
Variance on the kernel estimate is:
Proof:
  Since are uncorrelated,
  Substitute expressions for and

## Slide 28: Variance Error for a Uniform Kernel
Example: Uniform kernel
  Length
Suppose that there are reference signals in window
Variance error:
  Why?
Conclusion: Variance error decreases with kernel width
In general, increasing kernel width, decreases variance error
ref signal locations in window

## Slide 29: Bias Error
Signal error:
local average of
  Write as:
  Weighted average of values of
  Weights sum to one
Bias error, is large when:
  Average over region where changes significantly
  Window Coherence bandwidth / time
In general, increasing kernel increases the bias error
Low bias error
Kernel width Coherence BW
High bias error
Kernel width Coherence BW

## Slide 30: Bias-Variance Tradeoff
High variance Too low averaging
High bias
Too much averaging
Increasing kernel width
Decreasing kernel width

## Slide 31: Bias-Variance Tradeoff
High variance
Small kernel width Too low averaging
High bias
High kernel width
Too much averaging
Optimal
This example:
  Mean delay spread, ns
  Coherence BW, MHz
  Optimal width: subcarriers 135 kHz
  We see:

## Slide 32: Modeling Channel Estimation Error
Channel estimation error:
Channel estimation error has two components:
  Each term depends on level of averaging in the kernel estimator
Bias error:
  Typically scales with the channel power
  Since medium is linear, increasing TX power will not change the relative kernel error
  Assume
  Constant increases with the kernel width
Variance error:
  From earlier, we can write
  Constant decreases with the kernel width

## Slide 33: Effective Noise in Equalization
Consider channel on a single resource element:
  Channel:
  SNR is
Simple model for channel estimation error:
  Bias+ variance channel estimation error:
Consider equalized estimate:
  Total
  Neglecting cross terms:
Total effective noise, has two terms:
  Original noise:
  Distortion from channel estimation error:

## Slide 34: Signal-to-Noise and Distortion (SNDR)
Equalized symbol:
Signal energy:
Total effective noise energy:
  Error energy is
Signal-to noise and distortion (SNDR):
  Proof:
  Substitute in

## Slide 35: SNDR Regimes
SNDR:
Low SNR regime:
  Loss in SNR of
  Limited by variance error,
High SNR regime:
  Limited by bias error,
Low SNR Variance error loss
High SNR Bias error saturation

## Slide 36: Estimating Effective Noise
For equalization and LLR calculations we need to estimate the effective noise
Noise estimation can be performed via residual error:
  Reference symbols:
  Obtain channel estimate: (e.g., via kernel regression)
  Effective noise estimate:
Residual error estimate captures noise and distortion
  If then
But the residual error estimate is biased:
  Under-estimates the variance error in the distortion
  Measuring error on the symbols used in training
  Can compensate by scaling the noise estimate before using in the equalizer or demodulator

## Slide 37: Measuring True Effective Noise
From previous slide, residual error noise estimate is biased
  Under-estimates the variance error
  Uses training symbols for error estimation
To more accurately measure noise, use separate set of test symbols
  Get test symbols:
  These symbols are distinct from the RS used in training
  Error estimate on the test:
Rarely used during actual operation of the receiver
  Adding test symbols adds excessive overhead
But, the test symbols can be done in test and simulation
  For example, populate data symbols with known symbols

## Slide 38: Noise Estimation Simulation
Simulation parameters as before
  Mean delay spread, ns
  Coherence bandwidth, MHz
  One RS per 4 sub-carriers: 60 kHz
“True” noise measured on data symbols
  Not used in training
“Estimated” noise measured on RS symbols
We see:
  Estimated noise is slightly optimistic at low SNRs
  Both true and estimated noise levels off at high SNR
  Limited by bias SNR

## Slide 39: SNDR in Practice
Estimated the SNDR from effective noise estimate
In this simulation:
  About 0.4 dB loss at low SNRs
  About 27 dB saturation

## Slide 40: In-Class Exercise